HEADLINE
An Advanced Finite Element Model of IPMC
David Pugal
03/12/2008

---
Outline of the presentation
Basic model
3D meshing
3D model
Advancing the 3D model
Results

---
Background
IPMC – ionic polymer-metal composites are highly porous polymer materials, such as Nafion, filled with some kind of ionic conductive liquid
The polymer is coated with a thin metal layer
Electric fields causes the migration of ions inside the polymer → bending
The Finite Element Method

---
Headline
The basic model – ion migration
Nernst Planck equation:
Gauss's law:
Continuum mechanics
equations
{partial C} over {partial t} + nabla cdot (-D nabla C - z %mu C nabla %phi) = - {vec u} cdot nabla C
nabla vec E = {F cdot %rho} over {%varepsilon}

---
Actuation mechanism

---
Why 3D?
The resistance is dynamic
Expanding the one side of an IPMC causes higher resistances

---
3D meshing

---
3D meshing

---
3D model

---
3D model

---
Advancing the model
3D model without considering the surface resistance is rather overkill for calculations.
What we want to do:
  - Consider the current flow
  - Use it to calculate voltage drop in elements

---
Ramo-Shockley theorem
Ramo-Shockley theorem relates the charge movement in an environment to the current in circuit.
Used in plasma physics, ion channels, etc.
The general form is:
I = 1 over {1 Volt} sum from{i} q_i W(r_i) cdot v_i

---
Ramo-Shockley theorem
For parallel plates, the equation could be simplified:
Using the equation helps to simulate
  - local current densities
  - voltage changes in the electrodes – using the FEM domain specific approach.
I = S over d int from{0} to{d} j_p dx

---
The approach
To get a proof of concept model, the easier approach was used.
The 2D simulations were mapped into 3D:
2D flux was projected to 3D surface.

---
Conclusions and future work

---
Thank you,
Questions please.