## Slide 1: Dynamic Surface Resistance Model of IPMC
3/11/2009
David Pugala,b, Alvo Aabloob, Kwang J. Kima
a Active Materials and Processing Lab, Mechanical Engineering dept. University of Nevada, Reno
b IMS Lab, Tartu University, Estonia

## Slide 2: Outline
IPMC materials and the basic model
Extended Surface Resistance Model
  Theoretical considerations
  Possible applications
  Simulations using Finite Element Method
  Preliminary results
  Concerns
Future Work

## Slide 3: IPMC materials and the basic model
IPMC – ionic polymer-metal composite material
  Electric field
  Ion migration
  Current/charge driven bending
Polymer
backbone
Free cation

## Slide 4: IPMC materials and the basic model
Charge migration and diffusion description
  Nernst-Planck equation
Electric field – Gauss’ equation
  Rather simple way to describe the field
In this research, the bending is not considered explicitly

## Slide 5: IPMC materials and the base model
Meshing for 2D and 3D
2D mapped mesh
3D mapped mesh

## Slide 6: IPMC materials and the base model
The electric field and the cation distribution at t >> 0
  Given model gives somewhat high field values for t >> 0
  Otherwise the shape is physically reasonable

## Slide 7: IPMC materials and the base model
The base model calculations depend on the chosen underlying equations
  The Comsol Multiphysics is the modeling software
  The previous graph was the result of choosing electrostatic model with specified voltage on boundaries.
  The following graph is calculated using a general PDE formulation with specified field strengths*
* D. Pugal, K. J. Kim, A. Punning, H. Kasemagi, M. Kruusmaa, and A. Aabloo, “A self-oscillating ionic
polymer-metal composite bending actuator,” Journal of Applied Physics 103(8), p. 084908, 2008

## Slide 8: Extended Surface Resistance Model
The idea is to tie together current flowing through the surface and the ionic current inside the polymer.
The similar technique is used in
  Plasma physics *
  Ion channels in proteins #
Courtesy of Matthew Dingemans
# W. Nonner, A. Peyser, D. Gillespie, and B. Eisenberg, “Relating Microscopic
Charge Movement to Macroscopic Currents: The Ramo-Shockley Theorem
Applied to Ion Channels,” Biophysical Journal 87(6), pp. 3716–3722, 2004.
* P. Paris, M. Aints, M. Laan, and T. Plank, “Laser-induced current in air gap
at atmospheric pressure,”
Journal of Physics D: Applied Physics 38(21), pp. 3900–3906, 2005.
Courtesy of M. Laan

## Slide 9: Extended Surface Resistance Model
Ramo-Shockley theorem
  equates the total current (particle plus displacement) measured in the external circuit with the microscopic motion of the charged particles in the domain between the electrodes.
  The current flowing into an electrode held at voltage V
  By integrating over arbitrary trajectories, we can get the charge
  For the capacitor model, the following relation can be derived:

## Slide 10: Extended Surface Resistance Model
Electrodes as continuous media
  Electrodes could be considered as a set of finite resistors
    Currents would add as Kirchoff law states
  There exists a voltage drop along the resistors, therefore also along the whole electrode
  The voltage drop would be as a feedback in some sense – the less voltage at the end of the electrode results in a different cation profile inside the polymer
Rb
Rc
Rd
Re
Ra

## Slide 11: Extended Surface Resistance Model
Possible applications
  2D model
    Allows to consider surface resistance changes and respective voltage drops in the electrodes
    Different 2D electrode parameters could be considered
  3D model
    Allows modeling electrodes with more complicated surface characteristics – e.g. specific electrode shapes, laser altered surfaces, etc
  Calculation of heat generation on the electrodes.

## Slide 12: Extended Surface Resistance Model
Simulations using FEM
  Proof-of-concept simulations made with a small section of IPMC
  A base model without surface electrode. The arrows perpendicular to the surface denote the flux direction at the time t = 0.1

## Slide 13: Extended Surface Resistance Model
Simulations using FEM
  Added surface electrode.
  The blue-red area indicates the voltage on the grounded electrode and the blue equals to 0.

## Slide 14: Extended Surface Resistance Model
Preliminary results

## Slide 15: Extended Surface Resistance Model
Preliminary results

## Slide 16: Extended Surface Resistance Model
Some concerns
  For the variable resistance (3D), the calculation is too slow for the entire IPMC – must find ways to simplify
  Possible solutions:
    Do as many calculations as possible for small section of IPMC and extrapolate the results where possible
    Generate more efficient mesh – different powerful open source tools are available such as gmsh, etc.
  For instance, somewhat optimized mapped mesh for a 4cm x 1cm piece of IPMC results in ~100,000 DOF  large solution time ( > 30min)

## Slide 17: Extended Surface Resistance Model
Some concerns
  Direct usage of Ramo Shockley theorem is hard in time dependent simulations.
  The integration of current density is needed over the polymer subdomain
  That in turn requires free mesh (Comsol Multiphysics)  significantly increased calculation time.
  The possible solutions may include:
    Find different solver
    Use time stepping to include the currents and voltage drops (instead of full time dependent simulation)
    Further research coupling different domain
  Convergence problem when using the integrated value
    Weak-from solution

## Slide 18: Conclusions and Future Work
We have developed a base model to model the simple physical processes such as ion migration and electric field change in an IPMC
Extended model has shown some promising results for calculating currents in the electrodes.
The model has been shown to work in 3D as well.
Still some concerns must be addressed to get a fully functional model
More testing is needed.

## Slide 19: Thank You
Acknowledgements
  The authors from University of Nevada, Reno (UNR) acknowledge the financial support from the U.S. National Science Foundation (Award#: 0713075).
  We also acknowledge the financial support from
    The European Science Foundation DoRa programme
    RDF-ETF joint grant no. ESE1-2902-TR-07.

## Slide 20: Questions
Thank You and Questions please 