Characterization of Electromechanically Active Polymers using Impedance Spectroscopy

Indrek Must, Karl Kruusamäe, Urmas Johanson, Tarmo Tamm, Andres Punning, Alvo Aabloo

Intelligent Materials and Systems Lab, Institute of Technology, University of Tartu, Tartu, Estonia

Provide full correspondence details here including e-mail for the corresponding author

Provide short biographical notes on all contributors here if the journal requires them.

Characterization of Electromechanically Active Polymers using Impedance Spectroscopy

Sensors and actuators composed of electromechanically active polymer composites can be essentially improved by electrical modelling of these materials using impedance spectroscopy method.

Keywords: PCC, IPMC, position sensor

# INTRODUCTION

Electromechanically active polymers (EAP) are composite materials that exhibit changes in their size or shape when stimulated by an electric field. The most common applications of EAPs are actuators and sensors. Siia on vaja veel paar lauset ja viidet!

In the current paper we consider two types of ionic EAPs, which are rather similar in construction and operation, but are composed of different materials, and have substantial differences in operating mechanism. The materials considered are Ionic Polymer-Metal Composite (IPMC) and Carbon Polymer Composite (CPC). The common quality of the two materials is that they consist of polymer membrane, whose opposite planar surfaces are covered with layers of electrically conductive materials. The electric potential between the electrodes causes transverse movement of mobile ions inside the composite, forcing the actuator to bend. These actuators exhibit very large actuation at the low applied voltage (usually less than 3V).

These EAPs have also sensorial properties. Mechanical deformation induced by external forces causes transverse movement of ions inside the sheet; that in turn induces changes of electrical properties of different parts of the composite. These changes could be registered as short-circuit current between opposing electrodes or changes in impedance of different parts of composite. []

Ionic Polymer-Metal Composite (IPMC) is probably the best known type of ionic EAPs. The first publications about this material appeared in early 1990-s. IPMC consists if a thin membrane made of ionic polymer, covered by inert metal electrodes at the opposite planar sides. Ionic polymer contains suitable mobile counter-ions to balance the charge of the anions fixed to the polymer backbone, and solvent -typically water. Applied voltage causes the migration of cations inside polymer matrix, which in turn results with non-uniform distribution of the ions inside polymer. As a result, the polymer sheet bends. To avoid drying, these IPMC actuators are used in aqueous environment. A comprehensive review of the operating principles of IPMC can be found in [1], sensorial properties are thoroughly reviewed in [1-2]. The experiments described in the current paper were conducted with IPMC consisting of 0.25 mm thick Nafion® membrane covered with platinum electrodes. The introduced cations were Li+ .

In the recent years, the research on Carbon Polymer Composite (CPC; also PCC) materials has gained lot of interest and the research in a direction of finding the most perspective materials for this type of composite is of great significance. A CPC actuator is made of two layers of electrodes comprising carbon materials of high specific surface area. The electrodes are separated by a thin ion-permeable polymer film. The whole sandwich contains ionic liquid as electrolyte. The voltage applied between the carbon electrodes causes electro-osmotic effect in ionic liquid, which results in migration of the cations to one side of the material, and the anions to the opposite side. This results with different swelling of the electrodes and the whole material bends. CPCs are operated in ambient conditions. [3,4] In this paper, we describe experiments using CPC materials composed of carbide-derived carbon (CDC), Polyvinylidene fluoride (PVDF) polymer and 1-ethyl-3-methlyimidazolium tetrafluroborate (EMIBF4) as the ionic liquid.

Similar to supercapacitors for energy storage applications, EAPs are typically used at maximum possible working voltage (normally 3V) to maximize strain and force characteristics. Unfortunately, maximum voltages of impedance spectrometers typically do not exceed 1V. On higher working voltages, Faradaic processes are more likely to contribute to volumetric changes. IPMC materials typically use water as a solvent and are normally operated in aqueous environment to prevent from drying.

This article presents the impedance spectra of CPC and IPMC materials and their electrodes. The concept of using these two types of materials as position sensors is verified experimentally using impedance spectra. We also propose a methodology of describing the ageing effects of ionic EAPs with impedance spectroscopy.

# IMPEDANCE BEHAVIOR OF EAP MATERIALS

Impedance of nanoporous systems and systems comprising ionic liquid and/or ionic conductance is extensively described in the literature. []

Carbon-derived carbon is a microporous material with controlled pore size distribution and very high electric double-layer capacitance. The pores in the CPC material can be described as a transmission line with distributed ionic resistance and capacitance. Transmission line behaviour can be observed both between opposing electrodes and between opposing ends of one electrode layer.

In high frequency range, these types of materials behave as ideal resistors and in very low frequencies as ideal capacitors.

# SYSTEM SET-UP

There exist more than just one configuration of connecting the terminals of impedance measurement equipment to the ionic EAP material. In this work a systematic approach is used to describe electrode surface and cross-electrode impedances of IPMC and CPC materials.

An impedance spectrometer Parstat 2273, manufactured by Princetion Applied Research was used in experiments at frequencies 5 mHz  – 10 kHz, and the Precision Impedance Analyzer  6500B manufactured by Wayne Kerr Electronics at frequencies 20 Hz  – 100 kHz. All measurements with sinusoidal excitation were performed at 10 mV RMS.

Electrode impedance was measured by placing voltage terminals made of gold to opposite edges of one electrode layer of an assembled composite actuator (Figure 1: A). The effect of a separator and the opposing electrode layer was considered to be small, because the resistance between opposite edges of an electrode is known to be much smaller than between opposing electrodes. IPMC material was measured in hydrated state.

Impedance between the electrodes (hereinafter referred as cross-electrode impedance) was measured by placing clamp-shaped voltage terminals on opposing sides of one edge of an actuator (Figure 1: C). Again, it is apparent that the effect of surface impedance also contributes to this value.

Figure 1. Configuration for impedance measurement. Electrode impedance was measured by placing voltage terminals between opposing edges of one electrode layer (A) while applying straight, concave and convex shapes to the electrode (B). Cross electrode was measured between opposing sides of composite sheet (C) while bending the sheet to one or other (arbitrary) side (D)

Both, electrode and cross-electrode impedance were registered first in free deflection mode. After that, the composite sheet was bent to opposing sides to most equal bending curvatures possible ((Figure 1: B,D).  Bode plots of impedance magnitudes and phases were composed.

In ageing experiments of IPMC material, impedances were registered by placing a polymer sheet completely between voltage terminals with larger surface area than the sheet. Material degradation effects are important to know for practical applications and are so far not paid much attention to in the literature.

# RESULTS

Impedance plot of CPC electrode (figure 2) shows mainly resistive behaviour at high frequencies (>10 kHz) and more capacitive behaviour at lower frequencies. As expected, the impedance magnitude of an electrode in expanded state (convex side of an actuator) is more than twice of the magnitude compared to an electrode in free deflection state. This can be well interpreted with increase of distance between carbon particles next to each other. However, we can see that the electrode impedance magnitude also rises when the electrode is compressed (concave side of an actuator). We would normally expect an increase in conductivity in a compressed electrode as it has been already indicated in the case of IPMC material [David?]. Further on, from the impedance phase graph we can notice that we can get an increase in phase on expanded electrode and a decrease almost equal in extent on compressed electrode. From this data, we can conclude that it is possible to estimate the deflection of CPC actuator by registering phase behaviour.

Figure 2. Bode plot of CPC electrode in case of free deflection, concave (compressed) or convex (expanded) shape.

Figure 3. Bode and Nyqvist plot of IPMC electrode in case of free deflection.

Cross-electrode impedance spectrum of CPC material shows a strong increase in magnitude when sheet is bent on either (arbitrary) side. Although the sheet was bent to opposite sides to an equal extent, we can notice that the magnitude changes are very different. Figure 3 shows an exemplary behaviour of this type of material, but the proportions are unlike on different samples. We believe this behaviour has close connection with the behaviour of surface resistance described earlier. From the phase spectrum we can see that the phase declines in equal extent when bent to opposite sides. Cross-electrode impedance behaviour of IPMC material (Figure 4) shows a strong but almost equal change in impedance magnitude and phase when bent to opposing sides.

Figure 3. Bode plot of CPC cross-electrode impedance.

Figure 4. Bode plot of IPMC cross-electrode impedance.

# EQUIVALENT CIRCUITS

We propose the following equivalent circuits for both materials considered. The circuits depicted on figure 5 are composed of distributed elements both in surface and separating layer. Equivalent circuits between surface layers (electrode effects suppressed) can in case of both materials be described as double layer capacitance coupled with ionic resistance. Although, numeric values of both parameters can be different. Also, ohmic resistance (or solution resistance) is present in case of both materials. In case of CPC material, this value changes in very broad scale from one piece to another because the properties strongly depend on assembling parameters of the composite (distance between electrodes can vary).

Figure 5. Equivalent circuits of CPC and IPMC materials. Note an extra capacitance in the CPC electrode.

Mõõdetud parameetrite väärtuste vahemikud!

It has been reported earlier that capacitance component is present in IPMC material [Punn 2007] and CPC material [Takagi?] because discrete particles in the electrode are not perfectly in electrical connection. Capacitance originating from electric double-layer can be formed in parallel with resistance originating from direct contact of conductive particles. In case of CPC material, presence of an extra capacitance not connected in parallel with resistances is present. This indicates that between some particles in the electrode have no direct linkage and {they are charged through electric field}.

# AGEING EFFECTS

Ageing effects were performed on IPMC material.

When an IPMC material undergoes a large number of working (bending) cycles, various effects can occur. The metal cations associated with ionic groups in the polymer side-chains can be replaced by protons, therefore increasing (electronic) conductivity and resulting in the loss of ionic conductivity and decrease of deflection extent. Also, the polymer and electrode layer can be mechanically damaged and the material can be contaminated. It is possible to regenerate these materials by boiling in HCl solution for removal of contamination and reintroducing desirable ions after this.

To investigate such effects, an IPMC actuator which had been standing unused for 8 months was first applied 190000 cycles of sinusoidal excitation signal at 1.5 V. Impedance spectra were registered after cycling, after changing counter-ions to H+ and after regeneration process. From figure 6 we can notice that change of cations contained in the composite to protons, electronic (parallel) conductance increases in the order of one magnitude. Comparison of spectra before and after regeneration process reveals no noticeable change in impedance magnitude at all frequencies, but only moderate change in phase behaviour at high frequencies. The extent of deflection amplitude remained unchanged in the experiment.

Further on, the IPMC actuator was cycled at higher excitation amplitudes. From figure ??? it can be seen that cycling an actuator 3600 times at 2.8 V causes more changes in impedance spectra than 20000 cycles at 1.8 V.

Figure 6. Ageing of IPMC. Consecutive experiment was performed with a single IPMC actuator.

From this experiment, we can clearly notice that higher working voltages lead to faster degradation of this type of material. Electrolysis of water contributes more at higher potentials. In figure 7, voltage-current dependence of IPMC is presented in semilogarithmic scale. At potential of about 2.3 V the slope of the graph starts to increase rapidly, giving an evidence of more dominant redox processes on electrodes. An electrochemical window of water is known to be at 1.23 V. The reason for increase of suitable working potential in case of IPMC material by 0.97 volts is deficiency of hydrogen ions inside the ionic polymer membrane.

Figure 7. Voltage-current relationship of an IPMC actuator with water used as solvent.  Notice an increase in current at 2.3 V

# REGISTERING OF IMPEDANCES AT LOW FREQUENCY RANGES

Electromechanically active polymers considered in this article can be represented as a capacitance with huge numerical value which is charged or discharged through moderately high resistance. It is obvious that the characteristic area of impedance spectra is located at very low frequency range, often falling behind mHz range. The measurements at microhertz range are extremely time consuming and in some cases cannot be performed because it is probable that the system under test can change its properties during the time of measurement.

To overcome this problem, a straightforward approach is proposed here. A resistor with well-known electrical parameters is added in parallel with system under test. An extra resistor effect is subtracted from the result data. A diversity of equivalent circuits can be parameterized by this method using equivalent impedance conversion formulas found in the literature.

# REFERENCES

1.	Shahinpoor, M., Kim, K. J., “Ionic polymer–metal composites: I. Fundamentals”, Smart Materials and Structures 10(4), 819-833 (2001).

2.	Pugal, D., Jung, K., Aabloo, A., Kim, K., “Ionic polymer-metal composite mechanoelectrical transduction: review and perspectives”, Polymer International 59(3), 279-289 (2010).

3.	Torop, J., Kaasik, F., Sugino, T., Aabloo, A., Asaka, K., “Electromechanical characteristics of actuators based on carbide-derived carbon”, Proceedings of the SPIE 7642, 76422A (2010).

4.	Torop, J., Arulepp, M., Leis, J., Punning, A., Johanson, U., Palmre, V., Aabloo, A., “Nanoporous carbide-derived carbon material-based linear actuators,” Materials 3(1), 9-25 (2010).

5.	Punning, A., Johanson, U., Anton, M., Aabloo, A., Kruusmaa, M., “A Distributed Model of Ionomeric Polymer Metal Composite”, Journal of Intelligent Material Systems and Structures 20(14), 1711 - 1724 (2009).

6.	Punning, A.; Kruusmaa, M.; Aabloo, A.. “Surface resistance experiments with IPMC sensors and actuators”, Sensors and Actuators A: Physical, 133(1), 200 - 209 (2007).

7.	Kruusamäe, K.; Punning, A.; Kruusmaa, M.; Aabloo, A., “Dynamical variation of the impedances of IPMC”, Proceedings of SPIE 7287, 72870V (2009).

8.	Leary, S., Bar-Cohen, Y., “Electrical impedance of ionic polymeric metal composites”, Proceedings of SPIE 3669, 81-86 (1999).

9.	Chen, Z., Tan, X., “A control-oriented and physics-based model for ionic polymer-metal composite actuators”, IEEE/ASME Transactions on Mechatronics 13(5), 519 – 529 (2008).

10.	Takagi, K., Nakabo, Y., Luo, Z. W., Asaka, K., “On a distributed parameter model for electrical impedance of ionic polymer,” Proceedings of SPIE 6524, 652416 (2007).

11.	Nakamura, T., Ihara, T., Horiuchi, T., Mukai, T., Asaka, K., "Measurement and Modeling of Electro-Chemical Properties of Ion Polymer Metal Composite by Complex Impedance Analysis", SICE Journal of Control, Measurement, and System Integration 2(6), 373-378 (2009).

12.	Takeuchi, I., Asaka, K., Kiyohara, K., Sugino, T., Mukai, K., Randriamahazaka, H., “Electrochemical Impedance Spectroscopy and Electromechanical Behavior of Bucky-Gel Actuators Containing Ionic Liquids”, The Journal of Physical Chemistry C, 114, 14627–14634 (2010).

13.	Randriamahazaka, H., Asaka, K., “Electromechanical Analysis by Means of Complex Capacitance of Bucky-Gel Actuators Based on Single-Walled Carbon Nanotubes and an Ionic Liquid”, The Journal of Physical Chemistry C, 114, 17982–17988 (2010).

increase of ionic resistance (or double layer capacitance), which is caused by changes  of ionic mobility under elevated mechanical stress conditions

# Comments

Kas seda lõiku on üldse vaja?

See lõik ei ole veel eriti sisukas.

Mis see systematic approach tähendab?

Ma arvan et B ja D pole vaja, parem pane kolmandaks joonis kuidas ageing mõõdeti.