Low voltage linear actuators based on carbide derived carbon powder

Janno Torop(a), Mati Arulepp(a,b), Jaan Leis(b,c), Andres Punning(a), Urmas Johanson(a), Alvo Aabloo(a)

(a) ‘IMS Lab, Institute of Technology, University of Tartu, Nooruse 1, 50411 Tartu, Estonia

(b) Carbon Nanotech Ltd, Riia 185, 51014 Tartu, Estonia

(c) Institute of Chemistry, University of Tartu, Viljandi 42, 50411 Tartu, Estonia

Abstract

Novel linear electromechanical actuators based on nanoporous TiC-derived carbons was prepared and studied. Traditionally, thin membranes containing mobile ions inside are used for bending actuators. We describe a linear actuator which consists from carbon material thin films and ionic liquid. The thin film is made from nanoporous TiC-derived carbon powder and polytetrafluoroethylene (PTFE) as a binder agent. The working mechanism of the actuators is based on the interactions between the high-surface carbide derived carbon (CDC) and the ions of the electrolyte. These actuators are able to generate linear actuation of about 1% from their thickness under the voltage less than 3 V. The motion starts already at 0.8V and the magnitude of actuation depends on the electrical charge stored by the device. Two different types of electrolyte were used: 1) Ionic liquid (EMITf) and 2) Tetra-alcyl-ammonium salt in propylene carbonate (PC) solution. The actuators with ionic liquid have 60% higher movement. The electromechanical parameters of the actuators were studied by using cyclic voltammetry and electrochemical impedance spectroscopy methods.

# Keywords: Linear actuator, carbide-derived carbon (CDC), ionic liquid, electroactive polymer (EAP)

# INTRODUCTION

There is an increasing interest in using soft actuators in the field of biomimetic devices, since they mimic the behavior of biological muscles. The materials are attractive for creating artificial muscles used in biologically inspired robots, not least underwater robotic applications[,,. In other hand, microapplications like MEMS, microfluidics and engineered devices housing hydrogel valves, filters, and lenses,, as well as other soft material actuators that mimic natural movement in microfluidics There exists today an emerging scientific field, where several electroactive polymers[] are exploited for a great variety of applications. Mechanical actuators that simultaneously may provide high power densities and large force generation capacities are of great scientific and technological interest. There are several electroactive materials well-known. Electroactive polymer (EAP) transducers have large displacement under low bias (several volts). So far, EAP actuators have serious disadvantage in practical use due to low force. Several applications require small displacement with considerably high force, therefore piesoceramics are often used to generate micron scale actuation with large forcing output. Carbon/polymer thin sheets, main components of supercapacitors, provide micron scale displacement under low bias, contrary to piesoceramics which require high voltage. Supercapacitors are highly capacitive devices famous for their high power densities and energy efficiency up to 98% during charging-discharging cycle [Conway, Arulepp 2006]. In principal, the design of supercapacitors is comparable to ionic polymer actuators. They consist of two high surface area electrodes and separator in between. Porous polymer separator is a reservoir of electrolyte and avoids electronic conductance between electrodes.

We propose the material with linear actuation properties which consists from carbon material thin films and ionic liquid. The thin film is made from nanoporous TiC-derived carbon powder and polytetrafluoroethylene (PTFE) as a binder agent.

Carbon produced by extraction of metals from metal carbides is called carbide derived carbon(CDC) . The described method[Gogotsi Nature)] of carbon synthesis offers unique control over carbon microstructure and allows to fine-tune porosity at the nanoscale. Applications proposed for CDCs are fuel cells, hydrogen storage and different extraction/purification methods of noble gases based on the selective adsorption. However, main force of the development is focused to electrochemical storage devices, such are super- or ultracapacitors.

Fig. 1. A structure (a) and High Resolution Transmission Electron Microscope (HRTEM) picture (b) of amorphous microporous carbon.

Microporous amorphous carbons have non-uniform distribution of the curved graphene flakes as shown in Figure 1 (left)[Conway]. The High Resolution Transmisson Electron Microscope (HRTEM) picture of carbide-derived carbon as recorded with the transmission electron microscope (JEOL JEM 3010 operated at 300 kV) is shown in Fig. 1 (right) Carbon atoms have hybridization of sp2, but graphene forms 3D network. Advanced CDC materials have high electric double-layer (EDL) capacitance (130 F g-1 in non aqueous electrolyte). Hahn et al. performed dilatometric studies on the porous and graphitic carbon electrodes and observed significant reversible volumetric effects in the electrodes during the charging-discharging, results confirmed the electromechanical activity of porous carbon. The electroactive mechanism of carbon is based on the charging of electric double layer. The electric energy is stored by formation of double-layer at carbon/electrolyte interface, process is electrostatic and Faradaic reactions do not occur[Hahn]. Large capacity of porous carbon electrodes is provided by high specific surface area (typically 500 to 2000 m2g-1)[Gogotsi handbook].

The expansion of the carbonaceous electrodes is generally undesired and crucial factor for the cycle ability of energy storage devices. The dimensional changes, when they are non reversible during charging/discharging, may affect electric contact and causes tension accumulation in energy storage device. Faradaic charge-transfer reactions like those occur in batteries are often connected with non reversible dimensional changes, which can lead to reduction in charge capacity and ultimate failure of the device. Substantially higher stability and cycle life performance of advanced supercapacitors compared to batteries are generally ascribed in context that charge storage is based on pure double-layer charging, and not on Faradaic reactions. While batteries store the electrical energy in chemical bonds, EDL capacitors store it directly in the double-layer.We assume that transducers based on a high surface area carbide-derived carbon electrode material are suitable for short range displacement applications, because of proportional actuation response to the charge inserted and high Coulumbic efficiency due to EDL capacitance.

# Experimental Details

## Preparation of materials

Carbon powder

TiC-derived carbon powder, precursor of the actuator electrodes, was produced by Carbon Nanotech Ltd. TiC derived carbon is synthesized from titanium carbide by chlorination at high temperature (400 - 900 °C). Reaction product is amorphous carbon powder with particle size 2-5 m and large quantity of very small nanopores with pore size 6-9 Å in those powder particles.

Carbon-polymer film

The porous carbon electrodes films were prepared from the mixture of 92% (wt.) TiC-derived carbon powder and 8% (wt) PTFE binder polymer (Aldrich, 60% suspension in water) and rolled into to the thin active material sheet with a final thickness of 100 ± 5 m CDC powder (1g) was mixed with 6 mL of ethanol and added PTFE suspension in water to form slurry, which thereafter was gently pressed until a wet cake was formed. After evaporation of ethanol and water the cake was impregnated with heptane. A flatten carbon/polymer cake shaped to a multilayer cylinder and rolled in the axial direction of the cylinder. The latter procedure was repeated until elastic properties appeared to the carbon/polymer sheet. Finally, the heptane was removed at ~110 ºC. The carbon/polymer sheet was rolled stepwise down to the desired thickness, dried in vacuum owen at 170 ºC and coated from one side with a thin (~2 (m) aluminum layer, using Plasma Activated Physical Vapor Deposition. The electrode discs of desired size were cut from these sheets.  Importance of aluminum coating for reducing the contact resistance between carbon layer and current collector is studied and confirmed by Leis et al. [ja viide kus?].

## Assembling of the actuators

The linear actuators 1 – 4 (see Table 1) were assembled from the pairs of carbon electrode discs (Ø 1,7 cm), separated with an ion-permeable separator paper from Kodoshi Nippon (Fig. 2). Each actuator consisted of five electrode pairs with a total geometric surface area of 11.35 cm2. The electrode assembly was placed in the sealed aluminum container. The additional mechanical pressure (p=48 N cm-2) was applied by the spring through a special connecting rod. This rod was further used for measuring the linear movement of actuator by laser beam.

Fig. 2. The principal scheme of a linear actuator.

The actuator cells were vacuumed at 120 °C for 24 h before being impregnated with the electrolyte. The electrolytes used in this study were 1.0 M tetraethylammonium tetrafluoroborate in propylene carbonate (“Honeywell Digirena ®” TEABF4/PC, H2O < 0.003 %) and the ionic liquid 1-ethyl-3methyl-imidazolium trifluoromethane-sulfonate (EMITf, Fluka)

Table 1. The linear actuators tested in this study

| Actuator # | Notation of actuator | Notation of CDC material | Electrolyte |
| --- | --- | --- | --- |
| 1 | TEA600 | TiC-600 | 1.0 M TEABF4/PC |
| 2 | TEA800 | TiC-800 | 1.0 M TEABF4/PC |
| 3 | EMI600 | TiC-600 | EMITf |
| 4 | EMI800 | TiC-800 | EMITf |

## Electromechanical measurements

The test cell of the linear actuator is depicted in consisted of two fundamental parts – the electrochemical actuator and the optical detecting mechanism. The actuator is assembled in a sealed cell. The cell incorporates a spiral spring, compressing the actuator by the force of 100N. The optical system is mounted on the top of the cell. The mechanical coupling between the actuator and the optical system is implemented by a shifting vertical rod. The movement of the rod is transferred to the moving mirror using a steel eccentric and a lever. This mechanics magnifies the scale of movement of the actuator by 25 times. Further magnification of the scale is performed by a laser beam, reflecting from the mirror and targeted to a distant screen, as depicted in Fig. 3. The described optical system is able to magnify the scale of movement of the linear actuator by thousands of times, depending solely on the distance of the screen. In the course of the experiments the distance to the screen was a few meters and the expansion of the actuator by 1 (m was detectable as a displacement of the spot of the laser beam on the screen by 1 cm. The displacement of the spot on the screen was recorded by a high-speed firewire camera and the motion was thereafter digitalized using LabView software. Simultaneously, the electrical parameters - voltage and electric current – were recorded using National Instruments PCI-6034 DAQ card and LabView software. The electric current was measured as a voltage drop over the low resistance R. The EIS measurements were carried out with Solartron 1287 and 1255B AC frequency analyzer at AC signal 5 mV and fixed DC potentials 2.5 V and 1.5 V in frequency range of 1 MHz to 5 mHz.

The extent of actuation of the actuators in time-domain was detected using a custom-made optical system. The measurements were performed in two modes: (i) a constant current charge-discharge process (CC mode, triangular voltage spread in time). In CC mode we observed tendency of decreasing performance when actuators were charged relatively high current. To achieve maximum performance of actuators we combined constant current method with constant potential method (ii) (CCCP mode, rectangular voltage spread in time). Actuation is correlated and limited with the charge inserted in actuator.

Fig. 3. Illustration of the experiment setup.

# Results and Discussion

To study the actuators in detail, the CCCP mode was used. After charging the actuator to 1.5-3 volts using constant current IC (50, 100, 200, 400, 1000 mA), a constant potential VC (1.5, 2.0, 2.5, 3.0 V) was applied for up to 5 minutes. This method helps to examine the dynamics and the amplitude of actuation. During the period of the constant potential the current decreases substantially and the maximum amplitude appears in few minutes. In the course of different experiments the amperage of the constant current was varied in the range of 50 to 1000 mA.

Fig. 4. CCCP measurement of EMI800 (IC = 400 mA, VC = 2.5V)

The mechanical response of linear actuator EMI800(#4 in Table 1) under voltage 2.5 V (CCCP mode) is shown in Fig. 4a. The actuation amplitude reaches its maximum and remains stable in about 120 seconds, while the voltage reaches its stable level already in 60 seconds. This diagram is very typical, the similar behavior was observed in all tested actuators. The electrodes of the actuators TEA600 and TEA800 have same electrolyte 1.5 M tetraethylammonium tetrafluoroborate (C2H5)4NBF4 (TEA-TFB) in propylene carbonate (PC), but carbon powder is different. The actuator TEA600 was made from nanoporous TiC-derived carbon synthesized at 600ºC with the average pore size of APS = 9.3 Å, whereas carbon in the actuator TEA800 posses slightly increased APS of 10.2 Å. Density of TiC-600 carbon material is higher than TiC-800. The deviation in capacitance and response speed is caused by internal properties of carbon/polymer sheet and is not caused by ionic liquid properties. Pores of the material TiC-600 are 70 % smaller than 11 Å. In case the material TiC-800 corresponding value is 50 %. Hysteresis is observed during charging/discharging cycle (Fig 4b). Releasing of confined ions from pores depend an amount of ionic channels in small-diameter nanopores. Therefore increasing the amount of macropores in polymer-supported carbon electrodes may decrease hysteresis.

Electrolyte 1.5 M TEA-TFB in PC is commonly used in EDL capacitors because of its high conductivity a relatively small ion size, which gives a large capacitance. Ionic liquid EMITf was under study because of it is widely used as an electrolyte for IPMCs. EMITf has relatively high conductivity, low viscosity and it possess wide electric stability window. EMI+ and Tf  appear in ionic liquid as ion pairs with much higher ionic measurements, compared to TEA-TFB (TFB- = 4.8  Å, Tf - = 7.2 Å). TEA-TFB ions carry with them dynamic seath of specially adsorbed solvent molecules During the charging of electric double layer transport of electrolyte and ion recombination will take place. This process is limited by amount of active transport channels (macropores) and electrolyte viscosity. We assume that the dimensional change of actuator is consequence of charge injection in carbon nanopores during electric double-layer charging. The actuation-charge diagram shown in Fig. 4b indicates a nonlinear correlation between the actuation and electric charge stored and released during charging and discharging cycle of the actuator.

Fig. 5. CCCP measurement of EMI800 (IC = 1000 mA, VC = 3 V);a) voltage and current; b) actuation and charge

Fig. 5. depicts the series of periodic charging-discharging cycles of the actuator. As the charging current is high (1 A), the period of constant current decreases already in few seconds. During this time interval almost no movement is detected, since the voltage is low and the adsorption of ions is a diffusion-limited process in the porous electrodes. The current dies away slowly due to the internal resistance of the actuator. During discharging cycle the charge is released, current peak reaches up to 1.2 A and actuator shrinks. While discharging by a short-circuit, the adsorbed energy is wasted through the low ohmic discharge resistor. All studied actuators evolved an extraordinary current peak while discharging (see Fig 5a). These impulses of current can be stored and transferred to other devices. Improved enhancement of  the actuation did not substantially reduce the Coulumbic efficiency of linear actuators. In Tab 2 we can see measurement series of capacitance (Cs) and respective resistance (Rs) of actuators. Data was obtained from electrochemical impedance spectroscopy (EIS) measurements. EIS analysis is based on the Nyquist Z´´, Z´-plot method[viide], where Z´´ and Z´ are the imaginary and real parts of the complex impedance. Round-trip efficiency (RTE) or Coulumbic efficiency data was obtained using constant current (CC) charge/discharge regime. The energy efficiency of actuators depends from the value of cycling current. The delivered charge and capacitance decrease with increasing the current applied. EMI800 actuator exhibit normalized capacitance 121 F·g-1 and round trip efficiency 84 % at charging/discarging cycle between 0 - 3 V, with current 30 mA. Altough the capacitance of observed linear actuators does not reach to the advanced supercapacitors, all actuators demonstrated excellent electrical double-layer capacitance. The Coulumbic efficiency obtained in all studied linear actuators surpass electromechanical transducers based on ionic polymers

Polymer-supported carbon electrode materials have internal resistance, retarding propagation of electric field in electrode sheets. Capacitance of porous carbon material sheets is diffusion limited, which tending to exclude the quick actuation response. EIS measurements confirmed that all actuators behaved as a typical EDL capacitor. Diffusion rate and amount of confined ions in nanopores is related to the distribution speed of electric field in polymer-supported carbon 3D network. In the high-frequency region of AC the porous electrode behaves like a flat surface and therefore the capacitance obtained is by many orders of magnitude lower compared to the equilibrium capacitance at low frequencies. Therefore, charging and actuation in these devices can not be snap process.

The actuation of linear actuators at voltage 3 volts was obtained by 400 mA charging current (Tab 2.). Actuator EMI600 exhibit 60 % higher actuation in these condition. Considerably higher displacement of EMI600 can be explained by relatively larger ions in EMITf compared to TEA-TFB. Larger ions evoke extensive dimensional changes when enter into nanopores of porous carbon electrodes.

Table 2. The electrochemical parameters series capacitance (Cs), series resistance (Rs), round-trip efficiecy (RTE) and actuation of linear actuators.

| Notation of actuator | Cs [F g-1] | Rs [Ω∙cm2] | Actuation at 3 V [m] | RTE % |
| --- | --- | --- | --- | --- |
| TEA600 | 64 | 3.9 | 10.2 | 84 |
| TEA800 | 112 | 9.3 | 11.7 | 68 |
| EMI600 | 75 | 7.3 | 16.2 | 72 |
| EMI800 | 121 | 4.6 | 13.5 | 84 |

The actuation is correlated and limited with the charge inserted in actuator. Hahn et al[crossreference]expected that the charge specific expansion increases with the degree of graphitization and the apparent density of the carbon materials. They observed that the relative expansion of the graphitic carbon materials for a specific charge is larger than the respective expansion of microporous carbon materials. However, graphitic carbon materials demonstrated non reversible actuation due to ion intercalation process, which causing volumetric dimensional changes in these materials. Relatively low density and sparsity of 3D network of porous carbon electrodes are main properties providing good reversibility during cycling between 0-3 volts.

# CONCLUSIONS

We demonstrated the actuator for short range actuation applications capable to develop pressure 50 N·cm-2. Lifetime of the actuator is up to 106 cycles and energy storage efficiency approximately 90 % due to device is evolved from material commonly used in supercapacitors. Improvements in energy efficiency may accelerate the development of electromechanical actuators as well as provide industrial and consumer applications. Method for production carbon electrodes is efficient, it enables to prepare carbon/polymer sheets with final thickness 30 to 250 m (± 3%) and area of one sheet may reach up to 250 cm2. Using relatively low charging current values (less than 50 mA) linear dependence of charge inserted and actuation is observed. During continuous cycling good reproducibility of actuation were observed There are a lot of alternatives to produce porous carbon with controllable pore size in variation from 0.6 – 4 nm, which allows to attune porous carbon with suitable electrolyte to get high performance actuator. A challenging idea would be to test the extreme actuation in systems containing larger ions of electrolyte. Linear actuators based on CDC may attain success in micro application due to considerably high force.

ACKNOWLEDGMENT

We want to acknowlwdge the support from ……… Dr.Gunnar Svensson, Stockholm University, is thanked for the HRTEM study of carbon materials Our colleagues at Carbon Nanotech are thanked for assisting in the sample preparation and investigation

References

# Comments

Paremat sõna vaja?? Omadussõna mis kirjeldaks pasta taolist ollust

Siia oleks mikrojoonist vaja…

Kas tõesti kõik kolm asja, pinge vool ja liigutus olio vahemikus -1-+7 ?

Janno:On jah nii trehvanud, et kõik kolm suurust mahuvad ilusti graafikule

EIS aparatuur peab alguses oelma kirjadlatud, seal kus oli labview jne..

Artiklil vist vaja oma rferentide stiil panna: Style 	SPIE REFERENCES

# Endnotes

Y. Bar-Cohen (ed.), Biomimetics – Biologically inspired Technologies, CRC Press, Boca Raton, FL (2006).

Guo, T. Fukuda and K. Asaka, IEEE/ASME Trans. Mechatron. 8 (2003) 136–141.

N. Kamamichi, M. Yamakita, T. Kozuki, K. Asaka and Z.-W. Luo, Adv. Robotics, 21 (2007) 65–85.

Punning, A.; Anton, M.; Kruusmaa, M.; Aabloo, A. (2004). A Biologically Inspired Ray-like Underwater Robot with Electroactive Polymer Pectoral Fins. IEEE Confrence "Mechatronics and Robotics 2004" (MechRob04); Aachen, Germany; 13.-15.09.2004. Aachen: Eysoldt, 2004, (2), 241 - 245.

S. Collins, A. Ruina, R. Tedrake, M. Wisse, Science 2005, 307, 1082.

Aram J. Chung, Donn Kim and David Erickson, Lab Chip, 2008, 8, 330 – 338.

J. Y. Park, H. J. Oh, D. J. Kim, J. Y. Baek, S. H. Lee, J. Micromech. Microeng. 2006, 16, 656.

D. Kim, D. J. Beebe, Lab Chip 2007, 7, 193.

L. Dong, A. K. Agarwal, D. J. Beebe, H. R. Jiang, Nature 2006, 442, 551.

Gu Han Kwon, Joong Yull Park, Jeong Yoon Kim, Megan L. Frisk, David J. Beebe, and Sang-Hoon Lee, Small 2008, 4, No. 12, 2148–2153

Gogotsi, Y., Nikitin, A., Ye, H., Zhou, W., Fischer, J. E., Yi, B., Foley, H. C., Barsoum, M. W. Nanoporous carbide-derived carbon with tunable pore size. Nature Materials 2003, 2, 591-594

Hahn, M., Barbieri, O., Gallay, R., Kötz, R. A dilatometric study of the voltage limitation of carbonaceous electrodes in aprotic EDLC type electrolytes by charge-induced strain. Carbon 2006, 44, 2523

Hahn, M., Barbieri, O., Campana, F.P., Kötz, R., Gallay, R. Carbon based double layer capacitors with aprotic electrolyte solutions: the possible role of intercalation/insertion process. Appl. Phys. 2006, 633-638

Conway, B.E. Electrochemical Supercapacitors. Scientific Fundamentals and Technological Applications. Kluwer Academic, Plenum Publishers, New York, 1999

Gogotsi, Y (ed), Nanomaterials Handbook CRC Press, Boca Raton, FL (2006), 239-282.

Arulepp, M., Permann, L., Leis, J., Perkson, A., Rumma, K., Jänas, A., Lust, E. J. Power Sources 2004, 133, 320-328.

Arulepp, M., Leis, J., Läatt, M., Miller, F., Rumma, K., Lust, E., Burke, A.F. J Power Sorces 2006, 162, 1460-1466.

Leis, J., Arulepp, M., Kuura, A., Lätt, M., Lust, E. Carbon 2006, 44, 2122-2129.