

Abstract—This paper represents comparative results of hydrodynamic properties of a biomimetic underwater robot, fish and a submarine. The hydrodynamic properties are modeled with methods of computational fluid dynamics. In particular, we measure wake turbulence created by these natural and man-made objects. Our research is aiming at creating a biomimetic robot operating in shallow turbid waters near the bottom for volatile sediments and therefore we are interested in minimizing the turbulent flow.  The results of the computational fluid dynamics simulations show that the turbidity in a steady flow created by the model of our biomimetic robot is within the same range with fish and man-made streamlined underwater vehicles. It also gives us further guidelines for improving the design of our biomimetic underwater robot.

# INTRODUCTION

T

HE hydrodynamic model of an underwater robot permits us to determine the properties of the vehicle and facilitates the development of the control algorithms. The shape of the body determines the viscous drag of the vehicle and to a great extent the controllability of the robot. On the other hand the available technology sets constraints to the mechanical design of the robot. The constraints are set by the physical properties of the components, like weight and shape, and therefore in practice it is not possible to build a vehicle with ideal hydrodynamic properties. The irregularities and asymmetries of the body can change the hydrodynamic properties, in some cases, by even improving them [7]. We therefore view the design of the underwater vehicle as cyclic process where the hydrodynamic properties of the prototype are investigated theoretically, which in turn give suggestions of further improvements of the robot.

This paper represents a computational fluid dynamic (CFD) model of a biomimetic underwater vehicle and investigates its properties compared to a CFD model of a cone object, dolphin, manta ray and a submarine. The aim of this study is to get comparative data about hydrodynamic properties of those objects and guidelines to improve the design of the biomimetic underwater vehicle.

Due to the rapid increase of computational efficiency, the practical 3D CFD modeling is becoming increasingly popular as an efficient tool of investigating the hydrodynamic properties of robots [1]. Similar studies of comparing natural objects with artificial objects [5] or their components are made to investigate their hydrodynamic properties.

In this work we use free GPL software Gerris [2, 2a]. This software has been, for example, used to study ship turbulence [3]. It is a new generation software that exploits semi-structured quadtree/octree mesh models to increase computational speed without the loss of precision by permitting computation of the components of the model with a different precision. In this paper, we use a time-adaptive mesh to discretize the solution dynamically. This allows us to study time-dependent 3D Euler incompressible turbulent flow.

Mostly CDF modeling is performed using Reynolds averaged Navier-Strokes equations (RANS) and averaging is carried out in space and time. This solution has limited information about turbulence characteristics, because effects of turbulence are time-averaged.

In our simulations the averaging is done only spatially (Large Eddy Simulations-LES) and computational domain is discretized using cubic finite volumes that are organized as a spatial octree. This allows dynamic adaption of the spatial resolution to follow the evolving flow structures. In close of the robot the resolution is finest and faraway, only large structures are computed.

# The robot

Fig. 1.  The robot

The robot is a fin actuated biomimetic robot presented in Fig. 1. The robot is actuated by a tail fin and two side fins,   equipped with a color camera and sonars, compressed air supply and air chambers to change the buoyancy. It is designed to be used in a towed mode as well as in an autonomous mode. In the towed mode the side fins are used as horizontal rudders to change the altitude. In the autonomous mode the robot moves forward by the tail fin propulsions. The detailed description of the robot can be found in [teine icar paber].

The design considerations of the vehicle are task-specific. The vehicle is designed for visual inspection in shallow waters with low visibility and volatile sediments. Shallow water coastal regions often fall into this category, also inland water bodies (rivers, lakes, ponds, bogs) that often have a muddy bottom and low visibility. In these conditions it is important that the vehicle used for visual inspection creates as little turbulence as possible since the turbulent flow would beat up the silt from the bottom and decrease visibility.

Therefore we are interested in designing a vehicle that creates possibly little turbulent flow. The first choice is to use fin propulsion, apart from the classical choice of propelled locomotion, since it creates much less turbulence.

Besides the means of propulsion the vorticity of the wake also depends on the hydrodynamic properties of the vehicle itself.  Theoretically, we would like to design a vehicle with ideal hydrodynamic properties. Practically, we are constrained by the available technology, components, task specification, end user requirements, and cost factors. These CDF simulations permit us to evaluate the hydrodynamic properties of our vehicle and compare them to natural objects as well as man-made streamlined objects. Furthermore, it gives us guidelines to improve our vehicle’s design.

# models

We are interested in comparative assessments of the wake turbulence. We model and measure the wake turbulence of the following objects: the biomimetic underwater robot described in the previous section, an ideal cone, dolphin, manta ray and submarine.

To get the realistic 3D model of the underwater vehicle, the vehicle represented in Fig. 1 is photographed in the up-, side- and front view. The colored photos are converted to black and white images and converted to stl (stereolitography format) compatible with Gerris. The stereolitography images are converted to gtl (GNU Triangulated Surface) format by dividing the body to polygons. The model is corrected by hand in order to assure that there are no holes and gaps between the polygons. The resulting Bender CAD model is depicted in Fig. 2.

The models of the dolphin and the manta ray are retrieved from [4]. The model of the submarine is acquired from [9]. The Blender models are converted to stereolitography format and corrected by creating a new mesh with a polymender tool to compensate inaccuracies caused by conversions. Then the files are converted to gts format. The cone is created with Blender and saved to stl format.

Fig. 2. The Blender model of the underwater robot.

As water flows around an object, the uniform velocity field gets disturbed. The disturbance of the flow basically depends on the shape of the object and parameters of the flowing liquid. We are interested in the velocity field formed behind the vehicle, in the wake, because the disturbances at this region are most likely to beat up some silt from the bottom. For that reason, some simulations of water flow have been done to determine the circulation of the velocity of water behind an object, caused by the moving with a constant velocity. The velocity field is found with Gerris simulation software, as shown in Fig. XXX. The output is a grid with velocity vectors known at each square of the grid. To find the circulation of velocity (further denoted also as a circulation), a contour behind the object is chosen in x-y plane, and the following integral is calculated:

,										(1)

The numeric result of the integral is a velocity circulation by the definition and it is related to local vorticities as follows:

,					(2)

Where the term  is a local vorticity and vector ds is a local infinitesimally small surface area with the direction of normal to the surface. The circulation is calculated for several different objects for comparison.

Fig. X measured points

For comparability, all models are scaled down to the same length,  the water velocity of the simulations is set to 0,5 m/s,  water viscosity is set to 1, temperature is 20 degrees Celsius.

We measure the velocity and pressure in the area right ahead and behind of the body to find out if there are any changes and differences in these parameters.

The cone is chosen for modeling as an object creating large vorticities. It can be used as a reference to compare the characteristics of the robot to a non-streamlined body. ???The actual value of vorticity depends on the boundary conditions of (1)???. Do you mean: The actual value of the circulation depends on the chosen contour in (1). We tried to choose as similar contours as possible for all the objects. Since the cone creates turbulences larger at the sides and behind of the object, and less turbulence straight behind, we have defined the circulation to be measured between the points shown in Fig. X.

Other parameters we use for comparison are the pressure and the pressure difference in the front and behind of the object. For these measurements, we use only four points shown in Fig. X, one in the front of the object and three points behind the object.

# results

This section represents the experimental results. The cone was chosen as an object with poor hydrodynamic properties. This object is used as a reference to compare the simulation data. Figure X shows the 3D simulation of the cone. As mentioned above, for his object, the largest turbulence (or largest vortices??) is created quite far from the axis of symmetry.

Figure X shows the pressure change of the cone in four points with the given coordinates. Figure X shows the velocity circulation of the cone calculated over a rectangular trajectory behind the object defined by coordinates in Fig.x.

It can be seen that the circulation created by the cone varies heavily over time. This is the reason of changes in the pressure (the peak in Fig. X) and the large variance of the velocity.

Fig. X cone simulation

Fig. X cone pressure

Figures X, x, and X show the same simulation data for a model of a dolphin.

Fig. X dolphin in simulation

Fig. X Dolphin pressure changes

Fig. X Dolphin circulation

Fig. X robot in simulation

The same simulation data for the robot is represented in Fig. X, x and X.

The difference with the previous objects is that the pressure in front of the robot and behind of the robot now differs, being slightly less behind the robot. It has been investigated and demonstrated experimentally that fishes are passively moving forward against its own drag, being able to extract additional energy from the environment[REF?]. As the experiments have also been conducted with dead fishes, showing that the effect occurs also due to their body shape. The pressure difference (with the pressure being less behind the robot) indicates that due to the shape of the object, the Bernoulli force is created which induces a positive, upstream drag, thus making the swimming more efficient.

Fig. X robot pressure changes

Fig. X. robot circulation

Table I summarizes the numerical values of velocity circulations.

TABLE I

Numerical values of CIRCULATIONS

| Model | Circulation |
| --- | --- |
| cone | 3,012 |
| dolphin | -1,439 |
| robot | -0,886 |

# Conclusion

This paper presents comparative CFD simulations of ideal cone, fish and a biomimetic robot. The simulation results give us confidence that the underwater robot has acceptably good hydrodynamic properties. The velocity circulation of the water, caused by the robot, is large that of a dolphin but much less than of a non-streamline object chosen for a reference. On the other hand, the robot is chosen to create Bernoulli force which improves the efficiency of locomotion while the cone and the dolphin do not create such an effect.

Of course, the mechanical design of the robot is also influenced by technological constraints that do not permit to build a robot with ideal hydrodynamic properties. However, the simulation results are exploited further on to improve the design of the next prototype.

Appendix

Appendixes, if needed, appear before the acknowledg-ment.

Acknowledgment

The preferred spelling of the word “acknowledgment” in American English is without an “e” after the “g.” Use the singular heading even if you have many acknowledgments. Avoid expressions such as “One of us (S.B.A.) would like to thank ... .” Instead, write “F. A. Author thanks ... .” Sponsor and financial support acknowledgments are placed in the unnumbered footnote on the first page.

References

- G. O. Young, “Synthetic structure of industrial plastics (Book style with paper title and editor),” 	in Plastics, 2nd ed. vol. 3, J. Peters, Ed.  New York: McGraw-Hill, 1964, pp. 15–64.

- W.-K. Chen, Linear Networks and Systems (Book style).	Belmont, CA: Wadsworth, 1993, pp. 123–135.

- H. Poor, An Introduction to Signal Detection and Estimation.   New York: Springer-Verlag, 1985, ch. 4.

- B. Smith, “An approach to graphs of linear forms (Unpublished work style),” unpublished.

- E. H. Miller, “A note on reflector arrays (Periodical style—Accepted for publication),” IEEE Trans. Antennas Propagat., to be published.

- J. Wang, “Fundamentals of erbium-doped fiber amplifiers arrays (Periodical style—Submitted for publication),” IEEE J. Quantum Electron., submitted for publication.

- C. J. Kaufman, Rocky Mountain Research Lab., Boulder, CO, private communication, May 1995.

- Y. Yorozu, M. Hirano, K. Oka, and Y. Tagawa, “Electron spectroscopy studies on magneto-optical media and plastic substrate interfaces(Translation Journals style),” IEEE Transl. J. Magn.Jpn., vol. 2, Aug. 1987, pp. 740–741 [Dig. 9th Annu. Conf. Magnetics Japan, 1982, p. 301].

- M. Young, The Techincal Writers Handbook.  Mill Valley, CA: University Science, 1989.

- J. U. Duncombe, “Infrared navigation—Part I: An assessment of feasibility (Periodical style),” IEEE Trans. Electron Devices, vol. ED-11, pp. 34–39, Jan. 1959.

- S. Chen, B. Mulgrew, and P. M. Grant, “A clustering technique for digital communications channel equalization using radial basis function networks,” IEEE Trans. Neural Networks, vol. 4, pp. 570–578, July 1993.

- R. W. Lucky, “Automatic equalization for digital communication,” Bell Syst. Tech. J., vol. 44, no. 4, pp. 547–588, Apr. 1965.

- S. P. Bingulac, “On the compatibility of adaptive controllers (Published Conference Proceedings style),” in Proc. 4th Annu. Allerton Conf. Circuits and Systems Theory, New York, 1994, pp. 8–16.

- G. R. Faulhaber, “Design of service systems with priority reservation,” in Conf. Rec. 1995 IEEE Int. Conf. Communications, pp. 3–8.

- W. D. Doyle, “Magnetization reversal in films with biaxial anisotropy,” in 1987 Proc. INTERMAG Conf., pp. 2.2-1–2.2-6.

- G. W. Juette and L. E. Zeffanella, “Radio noise currents n short sections on bundle conductors (Presented Conference Paper style),” presented at the IEEE Summer power Meeting, Dallas, TX, June 22–27, 1990, Paper 90 SM 690-0 PWRS.

- J. G. Kreifeldt, “An analysis of surface-detected EMG as an amplitude-modulated noise,” presented at the 1989 Int. Conf. Medicine and Biological Engineering, Chicago, IL.

- J. Williams, “Narrow-band analyzer (Thesis or Dissertation style),” Ph.D. dissertation, Dept. Elect. Eng., Harvard Univ., Cambridge, MA, 1993.

- N. Kawasaki, “Parametric study of thermal and chemical nonequilibrium nozzle flow,” M.S. thesis, Dept. Electron. Eng., Osaka Univ., Osaka, Japan, 1993.

- J. P. Wilkinson, “Nonlinear resonant circuit devices (Patent style),” U.S. Patent 3 624 12, July 16, 1990.

- IEEE Criteria for Class IE Electric Systems (Standards style), IEEE Standard 308, 1969.

- Letter Symbols for Quantities, ANSI Standard Y10.5-1968.

- R. E. Haskell and C. T. Case, “Transient signal propagation in lossless isotropic plasmas (Report style),” USAF Cambridge Res. Lab., Cambridge, MA Rep. ARCRL-66-234 (II), 1994, vol. 2.

- E. E. Reber, R. L. Michell, and C. J. Carter, “Oxygen absorption in the Earth’s atmosphere,” Aerospace Corp., Los Angeles, CA, Tech. Rep. TR-0200 (420-46)-3, Nov. 1988.

- (Handbook style) Transmission Systems for Communications, 3rd ed., Western Electric Co., Winston-Salem, NC, 1985, pp. 44–60.	Motorola Semiconductor Data Manual, Motorola Semiconductor Products Inc., Phoenix, AZ, 1989.

- (Basic Book/Monograph Online Sources) J. K. Author. (year, month, day). Title (edition) [Type of medium]. Volume(issue).	 Available: http://www.(URL)

- J. Jones. (1991, May 10). Networks (2nd ed.) [Online]. Available: http://www.atm.com

- (Journal Online Sources style) K. Author. (year, month). Title. Journal [Type of medium]. Volume(issue), paging if given.	  Available: http://www.(URL)

- R. J. Vidmar. (1992, August). On the use of atmospheric plasmas as electromagnetic reflectors. IEEE Trans. Plasma Sci. [Online]. 21(3). pp. 876—880.   Available: http://www.halcyon.com/pub/journals/ 21ps03-vidmar

# Footnotes

	Manuscript received Feb. 15, 2007. This work was supported in part by Estonian Science Foundation Grant No. 6765, Estonian Environmental Investment Center and Netbell Ltd.

M. Listak is with Tallinn University of Technology, Dept. of Computer Engineering,  Raja 15, Tallinn, Estonia ; e-mail: madis.listak@mail.ee.

M. Kruusmaa is with the Tartu University Institute of Technology, Nooruse 1, 50411, Tartu, Estonia e-mail: maarja.kruusmaa@ut. ee.

# Text boxes

Template for Preparation of Papers for IEEE Sponsored Conferences & Symposia

Madis Listak, Maarja Kruusmaaa, Deivid Pugal, ???